## Slide 1
CHAPTER 2: PROCESSES AND STORAGE OF WATER IN THE ATMOSPHERE AND VEGETATION ZONE
    2.1 Important concepts and definitions in hydrology
    2.2 The hydrologic cycle
    2.3 Water balance
    2.4 Precipitation: Forms, Occurrence, Measurement and Analysis
    2.5 Runoff, Hydrograph, and Stream gauging
    2.6 Interception, Evaporation, and Transpiration

## Slide 2
1. Important concepts and definitions in hydrology
Related terms and definitions to hydrology
  Weather- “the state of the atmosphere with respect to heat or cold, wetness or dryness, calm or storm, clearness or cloudiness”
  Climate – “the average course or condition of the weather at a place usually over a period of years (usually about 30 years) as exhibited by temperature, wind velocity, and precipitation”.
    The reason is that the pattern of variation of meteorological data over time repeats itself in a period of about 30 years.
  Weather refers, generally, to day-to-day temperature and precipitation activity, whereas climate is the term for the average atmospheric conditions over longer periods of time (usually 30 years).

## Slide 3: Cloud Type Based On Properties
Cloud is a visible set of drops of water and fragments of ice suspended in the atmosphere and located at some altitude above the earth’s surface
Four basic cloud categories:
  Cirrus --- thin, wispy cloud of ice.
  Stratus --- layered cloud
  Cumulus --- clouds having vertical development.
  Nimbus --- rain-producing cloud
These basic cloud types can be combined to generate ten different cloud types, such as cirrostratus clouds that have the characteristics of cirrus clouds and stratus clouds.

## Slide 4: Cloud Types Based On Height
If based on cloud base height, the ten principal cloud types can then grouped into four cloud types:
  High clouds -- cirrus, cirrostratus, cirroscumulus.
  Middle clouds – altostratus and altocumulus
  Low clouds – stratus, stratocumulus, and nimbostartus
  Clouds with extensive vertical development – cumulus and cumulonimbus.

## Slide 6: Classification of clouds

## Slide 7
Reading assignment
  What is atmosphere?
    Vertical structure of atmosphere and its temperature
    General Circulation of the Atmosphere
    Pressure Belts and Wind Systems of the Earth
  What is Lithosphere?
  What is Biosphere?
  What is the Hydrosphere?
    What is hydrologic cycle?
    What are the specific properties of water?

## Slide 8
THE ATMOSPHERE
  The atmosphere is closely related to hydrology in a fundamental manner.
  It will, therefore, be appropriate to make a brief introduction to the subject of atmosphere.
  The Earth’s atmosphere is a complex fluid system of suspended particles and gases.
  These gases have been originated slowly over the geological ages from the interior of the solid earth by large scale volcanic activity
  The atmosphere of the earth, therefore, consists of gases, water vapor as well as solid and liquid particles.

## Slide 9
The boundaries of the atmosphere are not easily specified, although in this fluid system, shapes of gases envelope the Earth.
They can be arbitrarily delimited as the interface of Earth/atmosphere and atmosphere/space, but it should be mentioned that these are excessive simplifications.
For example, although there is a zone of transition where the Earth and solar atmospheres merge, the atmosphere does not have any external edge.
Also, at the Earth/atmosphere interface, the atmosphere penetrates into the pore spaces and voids between the soil particles and regolith and is continuous with the so-called soil atmosphere.

## Slide 10
Gases such as nitrogen, oxygen, argon, carbon dioxide, and water vapor make up 99.9% of the total volume of the atmosphere.
Other elements of this system are suspended particles such as dust, water droplets, and the minor gases.
Through the atmosphere, the various gases’ proportions change very slowly over time, and hence, the atmosphere is not uniform, and the distribution of the component elements indicates that it has a layered structure.

## Slide 11
This vertical constituent of the atmosphere structure can be related mainly to the distribution of absorption of radiant energy and can be described in terms of the temperature variable.
According to major changes in temperature, the atmosphere is divided into layers
On the Earth’s surface, gravity pushes down the air layers; this push is called air pressure.
Ninety-nine percent of the atmosphere’s total mass is below 32 km.

## Slide 12
Model of the vertical structure of the atmosphere.

## Slide 13
Troposphere:
  It is the lowest layer of the atmosphere and contains about 75-80% of the atmosphere.
  The top of the troposphere is called the tropopause.
  The height of the tropopause varies with latitude and season
  The main characteristics of this layer are:
  more or less uniform decrease in temperature with height at the mean lapse rate of 6.5°C per km,
  increasing of wind speed with height,
  principal medium for the movement of mass (water as liquid, solid or gas, dust, and pollutants),
  energy (heat energy from the sun) and momentum (winds) over the earth’s surface,
  practically all weather phenomena, such as clouds and precipitation, take place.

## Slide 14
Stratosphere:
  The layers above the troposphere up to a height of about 50 km is called the stratosphere.
  The lower stratosphere has a remarkably stable and approximately isothermal temperature distribution (–60°C).
  The stratosphere contains about 97% of the ozone in the atmosphere.
  Ozone acts as a shield in the Earth’s surface.
  It absorbs ultraviolet radiation from the sun.
  This causes a temperature increase in the upper part of the layer.

## Slide 15
Mesosphere:
  Above the stratosphere is the mesosphere where temperature again decreases with increasing height, reaching a minimum at about 80 km (mesopause).
  Mesopause is the coldest layer of the atmosphere with a temperature of –80°C to –100°C
Thermosphere:
  The thermosphere is a very high temperature region
  It extends from the mesopause (80 km) to the outer edge of the atmosphere several hundred kilometers aloft.
  In this layer, the temperature is very high because ultraviolet radiation is turned into heat (temperatures often reach 2000°C or more).

## Slide 16
Atmospheric specific humidity also displays a characteristic vertical profile with maximum values in the lower levels and with a considerable decrease in height.
The air above the tropopause is nearly dry as a consequence.
This vertical division is primarily due to two processes.
  First, at the surface, evaporation is the main source of atmospheric water vapor.
  Secondly, a much larger quantity of water is in the warmer air close to the surface.
Saturation also leads to the formation of water or ice droplets, clouds, and eventually precipitation.
Because of the higher incoming radiations, the temperature reaches its maximum in equatorial regions at the surface of the Earth.

## Slide 17
GENERAL CIRCULATION OF THE ATMOSPHERE
  The Movement of Air
    Horizontal Motions: parallel to Earth’s surface (the everyday wind)
    Vertical Motions: perpendicular to Earth’s surface (up/down)
      Forced to rise mechanically (e.g., encountering a mountain range)
      due to changes of buoyancy

## Slide 18
Vertical Motions due to Buoyancy
When ρ’ < ρ, positive buoyancy, upward motion (convection)
When ρ’ > ρ, negative buoyancy, downward motion (subsidence)
When ρ’ = ρ, neutral buoyancy, no vertical motion

## Slide 19
Horizontal Motions
  Air/water will move from a region of high pressure to low pressure due to pressure gradient force
Fluid with horizontal pressure gradient
For given pressure, air tends to move horizontally from the region of higher-density cool air to the region of lower-density warmer air.

## Slide 20
The Driving Force: The Global Energy Distribution
Temperature should be highest in the tropics and lowest at the high latitudes

## Slide 21
Earth as Heat Engine
Atmospheric circulations are driven by the latitudinal radiation energy distributions that produces atmospheric temperature and density differences.
Atmospheric circulation carrying warm air toward the poles and colder air toward the equator, which help balances the energy

## Slide 22
  At the equator, the high temperatures make the air less dense.
  It thus tends to ascend before being transported poleward at high altitudes in the troposphere.
  This motion is compensated for at the surface by an equator-ward displacement of the air.
  On a motionless Earth, this big convection cell would reach the poles, impelling direct exchanges between the warmest and coldest places on Earth

## Slide 24
However, due to the Earth’s rotation, such an atmospheric structure would be unstable.
Consequently, the two cells driven by the ascendance at the equator, called the Hadley cells, close with a downward branch at a latitude of about 30°
The Earth’s rotation is responsible for a deflection toward the right in the Northern Hemisphere at the surface and due to the Coriolis force toward the left in the Southern Hemisphere of the flow coming from the mid-latitudes to the equator.
Coriolis Force – apparent force caused by the rotation of the earth. Causes objects to be deflected to the right of their path of motion in the Northern Hemisphere and to the left of their path of motion in the Southern Hemisphere
This results in easterly trade winds characteristic of the tropical regions

## Slide 26
What is Hadley (cell) Circulation?
  George Hadley – English physicist and meteorologist 1735 paper: “Concerning the Cause of the General Trade winds”
  Proposed theory of planetary-scale circulation cells
  Ocean surface heated by sun (most strongly immediately below the sun)
  Warm water warms air which becomes buoyant (think helium balloon => warm air wants to rise)
  Why does warm air rise?
    Less dense (lighter)
    Density = mass / volume

## Slide 27
Heating causes low pressure (warm and lifting air)

## Slide 28
Conservation of mass (matter)
Complete the “circulation”!

## Slide 30
Similarly high and low pressure would appear on the earth with an alternating rhythm of low pressure, high pressure, low pressure and high pressure at 0°, 30°, 60° and 90°, respectively
Temperature is extremely low in Polar Regions.
The air being cold and heavy throughout the year, a high pressure belt is formed in both the North Pole and South Pole regions.
At about 60º north and south latitude, the air moving from the polar cold meets the air coming from the subtropical high pressure belts.
This causes air to rise and low pressure belts around 60º are developed in both hemispheres.

## Slide 31
The major pressure belts with approximate latitudes within which they lie are
  belt of low pressure along the equator;
  belts of high pressure at about 30° north and south;
  belts of low pressure at about 60° north and south; and
  belts of high pressure at each pole:

## Slide 32: What is Hydrology?
Hydor + logos (Both are Greek words)
  “Hydor” means water and “logos” means study.
Hydrologic science deals with the waters of the earth, including their
  occurrence
  distribution
  circulation
  chemical and physical properties
  reaction with their environment
  relation to living things

## Slide 33: Hydrologic science cont...
It is a multi-disciplinary science since water interacts (i.e. it is important to and affected by)
physical processes
chemical processes
biological processes

## Slide 34
Hydrology is closely related to other natural sciences:
  Precipitation and evaporation require knowledge of climatology and meteorology
  Infiltration and evaporation require knowledge of soil science
  Transpiration requires knowledge of biological process
  Groundwater flow requires insights into geology
  Surface runoff requires knowledge of geomorphology
  Stream flow requires knowledge of fluid mechanics

## Slide 35
The figure shows the position of hydrologic science in the spectrum of basic sciences to water resource management. Hydrology is an interdisciplinary geoscience built upon the basic sciences of mathematics, statistics, physics, chemistry and biology

## Slide 36: The Hydrological Cycle
  The pathway of water as it moves in its various phases, through the atmosphere, land, and the ocean is known as the hydrological cycle.
  It is a process of water circulation between the atmosphere, hydrosphere, and lithosphere
  It can be considered at two major scales:
    Global scale, where the major elements are the oceans (97%), continents (0,02% as inland waters), and atmosphere (0,001%); and
    Basin scale (mesoscale), where the major elements are water fluxes between the atmosphere, biosphere and lithosphere.
    Mesoscale water circulation can be considered as the template for the quantification of fundamental ecological processes.

## Slide 37
A fundamental concept of the hydrologic cycle is that water is neither lost nor gained from the earth over time.
However, the quantities of water in the atmosphere, lithosphere and hydrosphere are constantly changing because of the dynamic nature of the hydrologic cycle.
A few facts to remember about the hydrologic cycle are as follows:
  Solar energy provides the energy that drives and sustains the cycling of water on earth.
  There is no beginning or end to the cycle.
  The supply of water on earth is constant, but the allocation of water in storage or in circulation can vary with time.

## Slide 38: Hydrological Cycle

## Slide 39: Hydrologic System
In engineering and management analysis, it is common to represent the different components of the hydrologic cycle as components of a complex systems into subsystems

## Slide 40: The watershed as a hydrologic system

## Slide 41: Stages/components of hydrological cycle
  Precipitation
  Infiltration
  Interception
  Depression storage
  Run-off
  Evaporation
  Transpiration
  Groundwater

## Slide 42
Some of the rain will drain across the landscape toward stream channels as overland flow (runoff).
Some of the rain will seep into porous soils through infiltration.
Below the land surface, the region where soil pores contain both air and water is called the unsaturated zone (zone of aeration, vadose zone).
Water stored in the unsaturated zone is called soil moisture (soil water). A measure of the amount of water in the soil is called the moisture content, or soil water content.

## Slide 43
Near surface soil moisture is extracted by roots, and is then transpired.
Transpiration is the process by which plants return moisture to the air.
Plants take up water through their roots and then lose some of the water through pores in their leaves.
Water in the unsaturated zone can also migrate back to the land surface to evaporate.
Evaporation is the process of returning moisture to the atmosphere.
Water on any surface, especially the surfaces of ponds, streams, rivers, lakes, and oceans, is warmed by the sun's heat until it reaches the point at which water turns into the vapor, or gaseous, form.

## Slide 44
Under some conditions, water can flow laterally in the unsaturated zone, e.g. through macro-pores, a process known as interflow.
Some water in the unsaturated zone is pulled downward by gravity drainage (percolation).
At some depth, the pores of the soil are saturated with water. The top of the saturated zone is called the water table
Water stored in the saturated zone is called groundwater.
It moves through the soil layer as saturated subsurface flow (baseflow, groundwater flow) until it discharges as a spring, seeps into a pond or stream, or the ocean.

## Slide 45: Ground water
Water in the zone of saturation.
Lies beneath the zone of aeration (vadose zone or soil moisture).
The water table is the top surface of the zone of saturation.
It fluctuates with topography (may be higher than elevation of land such as at a lake) and with rate of recharge (infiltration from surface plus migration in from side) versus rate of discharge (loss due to pumping and migration out).
Varies with changes in seasonal or daily precipitation.
Ground water is the most important source of fresh water today, not surface waters (lakes and rivers).

## Slide 46: Ground water

## Slide 47: What is Watershed Hydrology?
Different disciplines analyze and describe data based on different land-based units. For example,
  timber management employs the forest stand,
  agriculture uses pastures, fields, or grazing allotments, and
  urban land managers focus on the city or municipality.
In hydrology, the land unit is the watershed, which also may be referred to as a basin or catchment.

## Slide 48
Understanding how water is used and cycled through a watershed provides the foundation for understanding and describing how landscapes and water interact.
The most basic and essential tool for understanding these interactions is the hydrologic cycle which describes how water is stored and moves within and among watersheds

## Slide 49
Hence, Watershed hydrology is an interdisciplinary science that focuses on the union of landuse activities including forestry, grazing, agroforestry, agricultural cropping, mining and urbanization with the science of hydrology.
Understanding the hydrologic response to land use and management is paramount to sustain land and water resources for future generations.
Gaining this understanding requires that we are able to recognize:
  how human use of natural resources alters fundamental hydrologic processes
  how these changes in processes translate into water flow response from watersheds.

## Slide 50
The atmosphere redistributes evaporated water by precipitation and condensation
The biosphere is from the top of trees to the deepest roots that can partition the water in it into runoff, soil and groundwater storage, groundwater seepage, or evapotranspiration back to the atmosphere.
The hydrologic processes of the biosphere and their interactions with vegetation and soils are of interest in understanding the hydrology and management of watersheds
human activities can alter the magnitude of various watershed storage components including soil water, rivers, lakes, and reservoirs.
With the water budget approach, one can examine existing watershed systems, quantify the effects of management impacts on the hydrologic cycle, and in some cases predict or estimate the hydrologic consequences of proposed activities.

## Slide 51
Water balance (The Conservation Equations)
  A system (e.g., lake, watershed) is any conceptually-defined region of space capable of receiving a sequence of inputs of a conservative quantity storing some of that quantity, and discharging outputs of that quantity
  A conservative quantity is one that cannot be created or destroyed within the system, for example
    mass, energy
  The basic conservation equation states:
  The amount of a conservative quantity entering a control volume during a defined time period, minus the amount leaving the volume during the time period, equals the change in the amount of the quantity.

## Slide 52
This basic conservation equation is in fact a generalization of the conservation of mass, Newton's first law (conservation of momentum) and the first law of thermodynamics (conservation of energy)
Stated more simply
Amount in - Amount out = Change in storage
or
I - O = ΔS
This is only true
    for conservative substances (no reaction)
    defined control volumes
    defined time period ΔT

## Slide 53
Water balance examples
  Since the conservation equation is scale independent, we could apply it at
    a point, or field plot
    a lake
    a huge watershed (e.g.,Blue Nile, Awash)
    a continent
    the globe

## Slide 54
The regional water balance is the application of the water balance equation (conservation equation) to a watershed (or to any land area such as a state or continent).
One can write the water balance equation for watershed
ΔS = I - O
Inputs (I) Outputs (O)
Precipitation (P) Streamflow (Q)
Groundwater in (GWi) Evapotranspiration (ET)
Groundwaterout (GWo)
ΔS = I - O
ΔS = P + GWi - (Q + ET + GWo)

## Slide 55
Estimation of regional ET.
  One of the most common applications of the regional water balance approach is in estimating regional ET.
  assume that surface water divides are equal to groundwater divides, and take GWi as zero. Then we can rewrite water balance as
    P + GWi - Q - ET - GWo= 0
    Assume GWi - GWo are negligible. Then
    P - Q - ET = 0

## Slide 57
Example 1 Estimate the evaporation for a month for a lake of 500ha surface area. The mean discharge from the lake is estimated to be 1m3/s. The monthly rainfall is about 10cm. A stream flows with an average discharge of 2m3/s into the lake. The water level in the lake dropped about 5cm in the month. The seepage loss are negligible.
Solution:
  Monthly inflow, Q = 2*3600*24*30 = 51.84*105m3
  Monthly outflow, O = 1*3600*24*30 = 25.9*105m3
  Monthly rainfall, P = 0.1*500*10,000 = 5*105m3
  Change in storage, ∆S = -0.05*500*10,000 = 2.5*105m3
  From water balance:
  E = (5 + 51.84 – 25.9 – 0 – (2.5))*105 = 33.42*105m3
  E = 33.42*105/(500*104) = 0.6684m = 66.84cm

## Slide 58
Example 2
In a reservoir dam, the average area of water surface is 35 km2 for October, and at this time, average inflow and outflow to the reservoir are 15 and 20 m3/s, respectively. If precipitation is 10cm in October and the reservoir storage decreases 15 x 106m3 due to other phenomena, using a water balance equation calculate the evaporation during the month (take 30 days for a month) assuming that the groundwater state is constant

## Slide 59
Water is the most abundant substance on earth upon which all life on earth is dependent. Hydrology deals with the earth’s water in all its phases and is therefore a subject of great importance to society for the creation of liveable environment. Human activities such as cultivation on terraced lands, clearing of forests for different purposes, construction of roads, mining, over exploitation of groundwater, dumping wastes into rivers and reservoirs, and application of high fertilizer doses for achieving higher yields, etc., changes the pattern of distribution and circulation of earth’s water. As every inhabitant living on the earth belongs to a particular watershed, they are continuously influencing quantity/availability and quality of water by their actions, and the use of water. The protection, conservation, and management of water resources and water quality depend upon all of us understanding the basic concepts of hydrology as well as that of watershed and watershed health. To do so the understanding of the hydrologic cycle is very important