## Slide 1: Debremarkos University Debremarkos Institute of Technology
School of Electrical and Computer Engineering
Introduction to Power Systems

## Slide 2: 1. Introduction
Chapter one
Notes: <number>

## Slide 3: Reading Assignment
  Read and write a report for the following topics.
  1.1 Growth of Electric Power Systems
  1.2 Development of Electric Power System
  in Ethiopia
  1.3 Power System Focus areas
  1.4 The Power system Engineer
<number>

## Slide 4: 1.5 Power System Functional Zones
Power system is defined as a network of one or more generating units, loads and power transmission lines including the associated equipment's connected to it.
Power system have a high level of interconnection and operate over a wide range of voltages.
Electrical power engineering is concerned with generation, transmission, distribution and utilization of electric energy.
An electric supply systems can be broadly classified as:
  d.c. or a.c. system
  Overhead or underground systems
<number>

## Slide 5
Every power system has three major components
  Generation: source of power, ideally with a specified voltage and frequency
  Load: consumes power; ideally with a constant resistive value
  Transmission and Distribution system: transmits power; ideally as a perfect conductor
Generally power system has three functional zones
    Generation system
    Transmission system
    Distribution system
<number>

## Slide 6
<number>
Transmission system – the bulk transfer of power by high voltage links between main load centers
  The transmission lines are the connecting links between all the generating stations and the distribution systems
  Distribution system – the conveyance of power to the consumers by means of low voltage networks
  A distribution system connects all the individual loads in a given area to the transmission lines.
Generation system - involves the conversion of energy from a nonelectrical form (such as thermal, hydraulic, or solar energy) to electric energy.
  Electric power is generated in the range of 11 kV to 25 kV, which is increased by stepped up transformer to the main transmission voltage (66 kV to 400 kV or higher)
Notes: Power system I, 2012
<number>

## Slide 7: Flow of Generation, Transmission and Distribution
<number>

## Slide 8: Cont.…
<number>

## Slide 9: Cont.…
<number>

## Slide 10: Vertical Monopolies
Within a particular geographic market, the electric utility had an exclusive franchise.
Generation
Transmission
Distribution
Customer Service
In return for this exclusive
franchise, the utility had the
obligation to serve all
existing and future customers
at rates determined jointly
by utility and regulators
It was a “cost plus” business
<number>
Notes: <number>

## Slide 11: a) Power System Generation
Takes place in power plants which may be geographically dispersed.
A power plant may house more than one generating unit.
Most of the power plants are classified based on energy resource.
hydrocarbons((thermal )oil, coal,(gas turbine)natural gas)
Water
Solar
Nuclear
Chemical(battery &other resource(fuel cell))
Wind
Tidal (ocean type generating electrical energy)
<number>

## Slide 12: Types of power generating units
Sources of Power System Generation are:
    Conventional and
    Non conventional energy sources
1. Conventional energy source:
- a source of energy that has been widely used for many years.
  Thermal (coal, oil)
  nuclear and
  hydro generations are the main conventional sources of electric energy.
These methods of producing electricity are often referred to as conventional energy sources.
They are the more traditional or more commonly used sources of electrical energy.
<number>

## Slide 13: Hydro-power
Hydroelectric power generation involves the storage of a hydraulic fluid, water, conversion of the hydraulic (potential) energy of the fluid into mechanical (kinetic) energy in a hydraulic turbine, and conversion of the mechanical energy to electrical energy in an electric generator.
The term hydro-power is usually restricted to the generation of shaft power from falling water.
The power is then used for direct mechanical purposes to drive the turbine or, more frequently, for generating electricity.
<number>

## Slide 14: Cont.….
<number>
  A hydro-electric power station utilises the potential energy of water at a high level for the generation of electrical energy.
  Water head is created by constructing a dam across a river or lake. From the dam, water is led to a water turbine through the penstock.
  As the water falls through a certain height, its potential energy is converted into kinetic energy and this kinetic energy is converted to the mechanical energy by allowing the water to flow through the hydraulic turbine runner.
  The turbine drives the alternator which converts mechanical energy into electrical energy.
  Hydro-power now accounts for about 20% of world’s electric generation. Output depends on rainfall and the landscape.

## Slide 15: Hydropower Generation
<number>
Notes: <number>

## Slide 16
<number>

## Slide 17
<number>

## Slide 18
<number>
    Thermal Power stations
    A generating station which converts heat energy of coal combustion into electrical energy is known as a steam/thermal power station.
In thermal-electric power plants, electrical energy is produced by burning coal, oil, or natural gas
The heat released by the combustion of coal produces steam in a boiler at high pressure and temperature, which when passed through a steam turbine gives off some of its internal energy as mechanical energy and is condensed in a condenser to be fed into the boiler again.
The steam turbine drives the alternator which converts mechanical energy of the turbine into electrical energy.
This type of power station is suitable where coal and water are available in abundance and a large amount of electric power is to be generated.

## Slide 19
<number>

## Slide 20
<number>
Nuclear Power Station
  A generating station in which nuclear energy is converted into electrical energy is known as a nuclear power station.
  In nuclear power station, heavy elements such as Uranium (U-235) or Thorium (Th-232) are subjected to nuclear fission (the breaking up of nuclei of heavy atoms into two nearly equal parts with release of huge amount of energy is known as nuclear fission) in a special apparatus known as a reactor.
  The heat energy thus released is utilised in raising steam at high temperature and pressure. The steam runs the steam turbine which converts steam energy into mechanical energy.
  The turbine drives the alternator which converts mechanical energy into electrical energy.

## Slide 21: Cont.…
<number>
  The most important feature of a nuclear power station is that huge amount of electrical energy can be produced from a relatively small amount of nuclear fuel as compared to other conventional types of power stations.
  It has been found that complete fission of 1 kg of Uranium (U235) can produce as much energy as can be produced by the burning of 4,500 tons of high grade coal..

## Slide 22
<number>
2. Non conventional energy sources - energy refers to the sources that are identified few decades ago.
  Solar Energy
  Wind Energy
  Tidal & Wave Energy
  Biogas Energy
  Geothermal energy
Solar Energy
Solar energy is the main constituent of all the available energy sources.
The major source of renewable energy is the sun which is converted into different forms, e.g., solar radiation, wind, wave, etc.
Solar energy refers the direct use of the energy contained in sunlight (in the form heat and light)
The heat energy is used in solar heating devices like solar cooker, solar water heater, solar furnaces etc. The light energy is used in solar cells.

## Slide 23
<number>
Wind energy
All moving objects contain kinetic energy
The kinetic energy of the wind can be changed into other forms of energy, either mechanical energy or electrical energy through wind turbine generators.
How is electricity generated by wind turbine?
Wind blows over the angled blades and results in a turning force.
The force will turn the shaft gearbox and generator, which are all connected. The gearbox increases the rotational speed, enabling the generator to produce electricity.

## Slide 24
<number>
A single wind mill produces only a small amount of electricity. So a large number of wind mills in a large area are coupled together to produce more electricity in wind energy farms.

## Slide 25
.
<number>
Notes: <number>

## Slide 26: Geothermal
Geothermal energy originates from the inner core of the earth and it is evident on the earth's surface in the forms of volcanoes, geysers, and hot springs.
The deeper regions of the earth’s crust is very hot. This heat melts rocks and forms magma. The magma moves up and collects below at some places called Hot spots.
The underground water in contact with hot spot gets heated into steam at high pressure.
By drilling holes into hot spots the steam coming out can be used to rotate turbines of generators to produce electricity
It is known that the largest geothermal resource in Africa (i.e >1000 MW) is available in Ethiopia.
<number>

## Slide 27
<number>

## Slide 28: Geothermal Resource Map
<number>

## Slide 29: Geothermal
<number>

## Slide 30: Geothermal Aluto
<number>

## Slide 31
<number>
Tidal energy
The periodic rise and fall of sea level due to gravitational attraction of the moon causes tides.
A dam (barrage) is constructed at a narrow opening between the land and sea. The movement of water during high tide and low tide can be used to rotate the turbines of generators to produce electricity.

## Slide 32
<number>
Biogas energy
Biogas is the name applied to a gaseous product released from anaerobic decomposition of different bio-wastes.
In this process, organic wastes are anaerobically fermented by microorganisms.
The gas thus produced contains about 60% methane and 40% CO2.
Biogas can be produced from cow dung, leaf litter mixtures, animal excreta particularly dairy cattle, pig and sheep etc.

## Slide 33: b) Power transmission
Transmission networks:
  Connect generating plants to consumption points.
  Interconnect power pools
  HVAC
  HVDC
High voltage transmission offers;
  Lower transmission losses
  Lower line voltage drop
  High transmission capacity
  Lower capital and operating cost
<number>

## Slide 34
<number>
Comparison b/n d.c. and a.c. system for transmission
Transmission of electric power by high voltage d.c. system is superior to that by high voltage a.c. system in many respects:
  It requires only two conductors for transmission as compared to three for a.c. transmission
  No inductance, capacitance and phase displacement problem in d.c. transmission
  There is no skin effect in a d.c. system. Therefore, entire cross section of the line conductor is utilized
  A d.c. line has less corona loss and reduced interference with communication ckts
  For the same working voltage, the potential stress on the insulation is less in case of d.c. system than that in a.c. system. Therefore, a d.c. line requires less insulation
  The high voltage d.c. transmission is free from the dielectric losses, particularly in the case of cables
  In d.c. transmission, there are no stability problems and synchronizing difficulties

## Slide 35
<number>
Disadvantages:
  Electric power can not be generated at high d.c. voltage due to commutation problems
  The d.c. voltage can not be stepped up for transmission of power at high voltage
  The d.c. switches and ckt breakers have their own limitations
A.C. Transmission: now a days, electrical energy is almost exclusively, generated, transmitted and distributed in the form of a.c.
Advantages:
  The power can be generated at high voltages
  The maintenance of a.c. substations is easy and cheaper
  The a.c. voltage can be stepped up or stepped down by transformer with ease and efficiency. This permits to transmit power at high voltages and distribute it at safe potentials

## Slide 36
<number>
Dis - Advantages:
  An a.c. line requires more copper than a d.c. line
  The construction of a.c. transmission line is more complicated than a d.c. transmission line
  Due to skin effect in the a.c. system, the effective resistance of the line is increased
  An a.c. line has capacitance. Therefore, there is a continuous loss of power due to charging current even when the line is open
Distribution by a.c. system is undoubtedly superior to that by d.c. system as in a.c. system voltage control is easy by means of transformers
The best way is to employ a.c system for generation and distribution and d.c. system for transmission

## Slide 37: Power transmission equipments
Transformer
  Step up transformer
  Step down transformer
  Potential transformer
  Current transformer
Transmission lines
  Circuit breakers and isolators
  Shunt and series reactors and capacitors
  Lighting arrestors
<number>

## Slide 38: c) Distribution system general
Receives electrical energy from the HV/MV levels.
Supplies energy to consumers
  At MV/LV levels
  Single phase and/or three phase
Main equipment in the distribution system;
  Distribution transformer
  Feeder
  Switches
  Fuses
  Protective relays, lighting arrester, CT and PT.
<number>

## Slide 39: Cont…
<number>

## Slide 40: Some of the Transmission Line in EEU
<number>

## Slide 41: Cont.…
<number>

## Slide 42: Three Phase Transmission Line
<number>
Notes: <number>

## Slide 43: Load dispatch center/ LDC
<number>
Notes: <number>

## Slide 44: Major component of the power system
Power Transformer
Why step-up and step-down voltage necessary?
To transmit hundreds of megawatts of power efficiently over long distances.
Power at low voltages is also necessary to be used at a safe level in home appliances and most industrial equipment.
<number>

## Slide 45: Power transformers can be classified as:
Step-up transformers to be connected between the generator and the transmission line.
Step-down transformers connected between the transmission line and various electrical loads.
The transformer consists of two or more insulated windings wrapped around an iron core. By definition, the primary winding is the input winding, and the secondary winding is the output winding
<number>

## Slide 46: Example 230/132 kV Transformer
230 kV surge arrestors
132 kV surge arrestors
Oil Cooler
Radiators W/Fans
Oil pump
<number>
Notes: <number>

## Slide 47
Some other types of transformers are used in measuring voltage, current, and power flow in the power system.
The majorities are potential transformers and current transformers.
Potential transformers (PT) are single-phase transformers of special design, which step down the voltage to be measured to a safe value.
Current transformers (CT) step down the currents and have insulation adequate to isolate metering equipment and personnel from the line voltage.
One terminal of the secondary of both potential and current transformers is usually grounded for safety.
<number>

## Slide 48: Complications in power systems
No ideal voltage sources exist
Loads are seldom constant
Transmission system has resistance, inductance, capacitance and flow limitations
Simple system has no redundancy so power system will not work if any component fails
<number>
Notes: <number>