## Slide 1
Chapter 2 Network & Transport Layer
Part II Transport Layer

## Slide 2
Transport Layer Overview and Protocols
Provide logical communication between app processes running on different hosts
Transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
More than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 3
Transport vs. Network Layer
Network layer: logical communication between hosts
Transport layer: logical communication between processes
  Relies on, enhances, network layer services

## Slide 4
  Multiplexing, Demultiplexing
  Reliable data transfer
  Flow control
  Congestion control
Transport Services

## Slide 5
Multiplexing/Demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
Demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
Multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3

## Slide 6
UDP: User Datagram Protocol [RFC 768]
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
Connectionless:
  No handshaking between UDP sender, receiver
  Each UDP segment handled independently of others
UDP use:
  Streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
Reliable transfer over UDP:
  Add reliability at application layer
  Application-specific error recovery!

## Slide 7
UDP: Segment Header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
Length in bytes of UDP segment, including header
No connection establishment (which can add delay)
Simple: no connection state at sender, receiver
Small header size
No congestion control: UDP can blast away as fast as desired
why is there a UDP?

## Slide 8
TCP: Overview RFCs: 793,1122,1323, 2018, 2581
Full duplex data:
  bi-directional data flow in same connection
Connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state before data exchange
Flow controlled:
  sender will not overwhelm receiver
Point-to-point:
  one sender, one receiver
Reliable, in-order byte steam
Pipelined:
  TCP congestion and flow control set window size

## Slide 9
TCP Segment Structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 10
TCP Seq. numbers, ACKs
sequence numbers:
  byte stream “number” of first byte in segment’s data
acknowledgements:
  seq # of next byte expected from other side
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
incoming segment to sender
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender

## Slide 11
Connection Management
Before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 12
TCP 3-way Handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN

## Slide 13
TCP: closing a connection
Client, server each close their side of connection
  Send TCP segment with FIN bit = 1
Respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
Simultaneous FIN exchanges can be handled

## Slide 14
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
TCP: closing a connection
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB

## Slide 15
Congestion:
Informally: “too many sources sending too much data too fast for network to handle”
Different from flow control!
Manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
Principles of Congestion Control

## Slide 16
Two different factors can limit the rate at which a source sends data
The inability of the destination to accept new data
  Techniques that address this are referred to as flow control.
The number of packets within the subnet.
  Techniques that address this are referred to as congestion control
Flow Control and Congestion Control

## Slide 17
An approach that can be used at either the network or transport layers is
Rate control: this refers to techniques where the source rate is explicitly controlled based on feedback from either the network and/or the receiver
For example, routers in the network may send a source a "choke packet" upon becoming congested. When receiving such a packet, the source should lower it rate
Approaches to Congestion Control

## Slide 18
TCP implements end-to-end congestion control
TCP detects congestion via the ACK's from the sliding-window ARQ algorithm used for providing reliable service
When the source times out before receiving an ACK, the most likely reason is because a link became congested
  TCP uses this as an indication of congestion
    TCP will slow down the transmission rate
TCP controls the transmission rate of a source by varying the window size used in the sliding window protocol
Congestion Control in TCP