## Slide 1: Chapter Two
8051 Microcontroller

## Slide 2: Reading
Reading:
  Muhammad Ali Mazidi, Janice Gillispie Mazidi, Rolin D. McKinlay, “The 8051 Microcontroller and Embedded Systems using Assembly and C”, 2nd Edition, Prentice Hall

## Slide 3: CPU families used in microcontrollers
Microcontroller family defines the controllers architecture.
All microcontrollers of a family
  contain the same processor core and hence are code-compatible.
  they may differ in the additional components like the number of timers or the amount of memory.
There are numerous microcontrollers on the market: Intel 8051, Motorola MC68HC11, PIC, HC, AVR,ARM and others.

## Slide 4: CPU families used in microcontrollers
In 1981,Intel Corporation introduced an 8-bit microcontroller called the 8051(Intel refers to it as MCS-51)
The 8051 microcontroller family became widely popular after Intel allowing other manufactures to make and market any flavor of the 8051.
  but remaining code-compatible.
The 8051 family has the largest number of diversified suppliers: Intel, Atmel, Philips, AMD, Infineon and others.

## Slide 5: Overview of 8051 family
The 8051 is an 8-bit processor and it has
  128 bytes of RAM
  4K bytes of on-chip ROM
  Two 16-bit timers
  One serial port
  Four I/O ports, each 8 bits wide

## Slide 6: 8051 Microcontroller
CPU
Interrupt
Control
OSC
Bus
Control
4k
ROM
Timer 0
Timer 1
Serial
128 bytes
RAM
4 I/O Ports
TXD
RXD
External Interrupts
P0 P2 P1 P3
Addr/Data

## Slide 7: 8051 Family

## Slide 8: 8051 pin diagram
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
40
39
38
37
36
35
34
33
32
31
30
29
28
27
26
25
24
23
22
21
P1.0
P1.1
P1.2
P1.3
P1.4
P1.5
P1.6
P1.7
RST
(RXD)P3.0
(TXD)P3.1
(T0)P3.4
(T1)P3.5
XTAL2
XTAL1
GND
(INT0)P3.2
(INT1)P3.3
(RD)P3.7
(WR)P3.6
Vcc
P0.0(AD0)
P0.1(AD1)
P0.2(AD2)
P0.3(AD3)
P0.4(AD4)
P0.5(AD5)
P0.6(AD6)
P0.7(AD7)
EA/VPP
ALE/PROG
PSEN
P2.7(A15)
P2.6(A14)
P2.5(A13)
P2.4(A12)
P2.3(A11)
P2.2(A10)
P2.1(A9)
P2.0(A8)
8051

## Slide 9: I/O Ports
I/O pins are generally grouped into ports of 8 pins, which can be accessed with a single byte access.
Pins can either be input only, output only, or most commonly— bidirectional, that is, capable of both input and output.
Apart from their I/O capabilities, most pins have one or more alternate functions to save pins and keep the chip small.

## Slide 10: 8051 I/O ports
8051 MCU has four ports P0, P1, P2, and P3 and each use 8 pins

## Slide 11: 8051 I/O ports
Port 0 （pins 32-39）：P0（P0.0-P0.7）
  8-bit R/W - General Purpose I/O
  Or acts as a multiplexed low byte address and data bus for external memory design.
Port 1 （pins 1-8） ：P1（P1.0-P1.7）
  Only 8-bit R/W - General Purpose I/O
Port 2 （pins 21-28）：P2（P2.0-P2.7）
  8-bit R/W - General Purpose I/O
  Or high byte of the address bus for external memory design.

## Slide 12: 8051 I/O ports
Port 3 （pins 10-17）：P3（P3.0～P3.7）
  General Purpose I/O: if not used by the internal peripherals (timers) or external interrupts.

## Slide 13: Other pins
EA（pin 31）：external access
  The EA pin is connected to GND to indicate the code is stored externally.
  For 8051, EA pin is connected to Vcc.
PSEN（pin 29）：program store enable
  This is an output pin and is connected to the OE pin of the ROM.
ALE（pin 30）：address latch enable
  It is an output pin and is active high.
  8051 port 0 provides both address and data.
  The ALE pin is used for de-multiplexing the address and data when Port 0 is in use.

## Slide 14: ROM in 8051
The original 8051 microcontroller has 4K bytes on-chip ROM.
No member of 8051 family can have more than 64K bytes ROM:
  The program counter is a 16-bit register

## Slide 15: RAM in 8051
There are 128 bytes of RAM in the 8051(Assigned addresses 00 to 7FH)
The 128 bytes are divided into three different groups as follows:
  A total of 32 bytes from locations 00 to 1FH are set aside for register banks and the stack
  A total of 16 bytes from locations 20H to 2FH are set aside for bit-addressable read/write memory
  A total of 80 bytes from locations 30H to 7FH are used for read and write storage, called scratch pad.

## Slide 16: RAM of 8051

## Slide 17: Register Banks

## Slide 18: Register Banks
The 32 bytes from address 00 to 1F hex are divided into 4 banks of registers in which each bank has 8 registers, R0-R7.
Register bank 0 is the default when 8051 is powered up.
  That is by default RAM locations 0, 1,2,3,4,5,6 and 7 are accessed with names R0, R1, R2, R3, R4, R5, R6 and R7 when programing the 8051.
We can switch to other banks by use of the PSW(program status word) register.
  Bits D4 and D3 of the PSW are used to select the desired register bank.

## Slide 19: Program Status Word (PSW)
The program status word (PSW) register, also referred to as the flag register, is an 8 bit register.
Only 6 bits are used
  CY (carry), AC (auxiliary carry), P (parity), and OV (overflow).
  The PSW3 and PSW4 are designed as RS0 and RS1, and are used to change the register banks.
Program Status Word (PSW) Register
CY | AC | -- | RS1 | RS0 | OV | -- | P
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
MSB
LSB

## Slide 20: Program Status Word (PSW)
The carry flag (CY)
  Set whenever there is a carry out from the D7 bit.
  It is affected after an 8-bit addition or subtraction.
  It can also be set to 1 or 0 directly by instructions "SETB C" and "CLR C” respectively
Auxiliary carry (AC)
  indicates a carry from D3 to D4 during addition and subtraction operations.
The overflow flag (OV)
  set whenever the result of a signed number operation is too large, causing the high-order bit to overflow into the sign bit.

## Slide 21: Program Status Word (PSW)
The parity flag (P)
  The parity flag reflects the number of 1s in the A (accumulator) register only.
  If the register A contains an odd number of 1s, then P = 1. And
  P = 0 if A has an even number of 1s.
We can select the corresponding Register Bank bit using RS0 and RS1 bits.

## Slide 22: Stack in 8051
The stack is a section of RAM used by the CPU to store information temporarily.
The register used to access the stack is called the stack pointer (SP) register.
The stack pointer in the 8051 is only 8 bit wide, which means that it can take value of 00 to FFH.
When the 8051 is powered up
  the SP register contains value 07 RAM location.
  08 is the first location used for the stack by the 8051.

## Slide 23: bit-addressable RAM
16 byte locations from 20H to 2FH are bit addressable.
  Provide 128 bits (16*8) of RAM bit-addressability
  They are address as 0 to 127 Decimal (00h-7Fh)
  The bit addresses 0-7 are the first byte of internal RAM location 20H and bit addresses 8-0FH are second byte of internal RAM location 21H

## Slide 24: bit-addressable RAM
Example: Which byte of RAM each of the following instructions modify?
  a) Setb 42h
  b) Clr 0Fh
  c) Setb 05
Answer:
a) Bit 2 of RAM location 28H
b) Bit 7 of RAM location 21H
c) Bit 5 of RAM location 20H

## Slide 25: Timers and Counters
Timers and counters are distinguished from one another largely by their use, not by their logic.
Both are built from adder logic with registers to hold the current value, with an increment input that adds one to the current register value.
  A timer has its count connected to a periodic clock signal to measure time intervals.
  A counter has its count input connected to an aperiodic signal in order to count the number of occurrences of some external event.

## Slide 26: Timers in 8051
Original 8051 has 2 timers.
Timers increment on each system clock.
Timer registers (TH0, TL0, TH1, TL1) can be read or written to.
Timer overflow can cause “interrupts” or set SFR bits high.
16 bits
TH0 : TL0
Timer 0
16 bits
TH1 : TL1
Timer 1

## Slide 27: Interrupts
There are two techniques which can be used by the processor to communicate with I/O(peripheral) devices: Polling and Interrupt.
  Polling: In this technique the processor polls the device (asks question) repeatedly at regular intervals to check if the device has completed the given task or has any new task to execute.
  Interrupt: An interrupt is a signal sent from a peripheral to the processor. A peripheral may send an interrupt signal to a processor when it has some job to perform which requires the processor’s intervention.

## Slide 28: Interrupts Vs Polling
An interrupt is like a shopkeeper. If one needs a service or product, he goes to him and tells him his needs.
  In case of interrupts, when the flags or signals are received, they notify the controller that they need to be serviced.
The polling method is like a salesperson. The salesman goes from door to door while requesting to buy a product or service.
  Similarly, the processor keeps monitoring the flags or signals one by one for all devices and provides service to whichever component that needs its service.

## Slide 29: Interrupts
An interrupt is an event that disrupts the normal execution of a program and causes the execution of special instructions.
Interrupt signals can cause a program to suspend itself temporarily to service the interrupt by branching into another program called Interrupt Service Routines (ISR) for the specified device which has caused the interrupt.
When the ISR completes, the processor returns to the work that was interrupted.
The interrupts can be either hardware interrupts or software interrupts.

## Slide 30: Hardware Interrupts
Hardware Interrupts: A hardware interrupt is an electronic alerting signal sent to the processor from an external device, like a disk controller or an external peripheral.
  For example, when we press a key on the keyboard, it triggers hardware interrupt which causes the processor to read the keystroke.

## Slide 31: Software Interrupts
Software Interrupts: A software interrupt is caused either by an exceptional condition or a special instruction in the instruction set which causes an interrupt when it is executed by the processor.
  For example, if the processor's arithmetic logic unit runs a command to divide a number by zero, to cause a divide-by-zero exception, thus causing the computer to abandon the calculation or display an error message.
  Software interrupt instructions work similar to subroutine calls.

## Slide 32: Interrupt Service Routine (ISR)
For every interrupt, there must be an interrupt service routine (ISR), or interrupt handler.
When an interrupt occurs, the microcontroller runs the interrupt service routine.
For every interrupt, there is a fixed location in memory that holds the address of its interrupt service routine, ISR.
  The table of memory locations that holds the addresses of ISRs is called the Interrupt Vector Table.

## Slide 33: Steps to Execute an Interrupt
When an interrupt gets active, the microcontroller goes through the following steps:
  The microcontroller closes the currently executing instruction and saves the address of the next instruction (PC) on the stack.
  It jumps to the memory location of the interrupt vector table that holds the address of the interrupts service routine.

## Slide 34: Steps to Execute an Interrupt
  The microcontroller gets the address of the ISR from the interrupt vector table and jumps to it.
    It starts to execute the ISR until it reaches the last instruction of the subroutine which is RETI (return from interrupt).
  Upon executing the RETI instruction, the microcontroller returns to the location where it was interrupted.
    First, it gets the program counter (PC) address from the stack by popping the top bytes of the stack into the PC.
    Then, it start to execute from that address.

## Slide 35
Interrupt
Program
time t

## Slide 36
Program
Interrupt Service Routine
Interrupt
Program
time t

## Slide 37: Interrupts in 8051
CPU
Interrupt
Control
OSC
Bus
Control
4k
ROM
Timer 0
Timer 1
Serial
128 bytes
RAM
4 I/O Ports
TXD
RXD
External Interrupts
P0 P2 P1 P3
Addr/Data

## Slide 38: Interrupts in 8051
There are six interrupts including RESET in 8051.
  Interrupt
  Reset
  External Interrupt 0
  Timer 0 overflow
  External Interrupt 1
  Timer 1 overflow
  Serial

## Slide 39: Enabling and Disabling an Interrupt
Upon Reset, all the interrupts are disabled even if they are activated.
The interrupts must be enabled using software in order for the microcontroller to respond to those interrupts.
A special function register called IE (interrupt enable) register is responsible for enabling and disabling the interrupt.
  IE is a bit-addressable register.

## Slide 40: IE (Interrupt Enable) Register of 8051
EA | -- | -- | ES | ET1 | EX1 | ET0 | EX0
EA (IE.7) – Enable All interrupts.
ES (IE.4)– Enable Serial port interrupt.
ET1 (IE.3)– Enable Timer 1 interrupt.
EX1 (IE.2)– Enable External 1 interrupt.
ET0 (IE.1)– Enable Timer 0 interrupt.
EX0 (IE.0) – Enable External 0 interrupt.
MSB
LSB

## Slide 41: IE (Interrupt Enable) Register of 8051
To enable an interrupt, we take the following steps:
Bit D7 of the IE register (i.e EA) must be high to allow the rest of register to take effect.
The value of EA
  If EA = 1, interrupts will be enabled and will be responded to, if their corresponding bits in IE are high.
  If EA = 0, no interrupts will respond, even if their associated pins in the IE register are high.

## Slide 42: Interrupt Priorities
What if two interrupt sources interrupt at the same time?
Each interrupt source can also be individually programmed to one of the two priority levels by setting or clearing a bit in the SFR named IP (Interrupt Priority).
A low-priority interrupt can be interrupted by a high-priority interrupt.
If two interrupt requests of different priority levels are received simultaneously, the request of higher priority is serviced.

## Slide 43: Interrupt Priority in 8051
If interrupt requests of the same priority level are received simultaneously, an internal polling sequence determines which request is serviced.
When the 8051 is powered up, the priorities are assigned according to the following.

## Slide 44: IP(Interrupt Priority) Register of 8051
We can alter the sequence of interrupt priority by assigning a higher priority to any one of the interrupts by programming the IP (interrupt priority) register.
To give a higher priority to any of the interrupts, we make the corresponding bit in the IP register high.
When two or more interrupt bits in the IP register are set to high:
  While these interrupts have a higher priority than others, they are serviced according to the sequence of priorities when the microcontroller powered on.

## Slide 45: IP(Interrupt Priority) Register of 8051
-- | -- | -- | PS | PT1 | PX1 | PT0 | PX0
PS (IP.4)–Defines the Serial port interrupt priority level.
PT1 (IP.3)– Defines the Timer 1 interrupt priority level.
PX1 (IP.2)– Defines the External Interrupt 1 priority level.
PT0 (IP.1)– Defines the Timer 0 interrupt priority level.
PX0 (IP.0) – Defines the External Interrupt 0 priority level.
MSB
LSB

## Slide 46: Registers in 8051
Most of 8051 register are 8-bit registers.
The most widely used registers
  A (Accumulator)
    For all arithmetic and logic instructions
  B, R0, R1, R2, R3, R4, R5, R6, R7
  PC (program counter)is 16 bits register

## Slide 47: Assembly languages
CPU can work only in binary.
  A program that consists of 0s and 1s is called machine language.
Assembly languages provided mnemonics for the machine code instructions.
  Low-level language, deal directly with the internal structure of the CPU.
Assembler is program used to translate assembly language program into machine code.

## Slide 48: Structure of Assembly Language
A given Assembly language program is a series of statements, or lines of
  Assembly language instructions
    Tell the CPU what to do
  Directives
    Give directions to the assembler
    do not generate any machine code and are used only by the assembler
An Assembly language instruction includes:
  A mnemonic (abbreviation easy to remember)
    The commands to the CPU, telling it what to do with those items.
  Optionally followed by one or two operands
    The data items being manipulated

## Slide 49: Assembly language instruction
An Assembly language instruction consists of four fields:
[label : ] mnemonic [operands] [;comment]
The label field allows the program to refer to a line of code by name.
A mnemonic-The commands to the CPU, telling it what those to do with those items.
Operands-The data items being manipulated.
Comments may be at the end of a line or on a line by themselves.
  The assembler ignores comments

## Slide 50
ORG 0H ;start(origin)at location 0
MOV R5, #25H ;load 25H into R5
MOV R7, #34H ;load 34H into R7
MOV A, #0 ;load 0 into A
ADD A, R5 ;add contents of R5 to A
ADD A, R7 ;add contents of R7 to A
ADD A, #12H ;add to A value 12H
HERE: SJMP HERE ;stay in this loop
END; end of asm source file

## Slide 51: Assembler directive
ORG (origin)
  The ORG directive is used to indicate the beginning of the address.
  The number that comes after ORG can be either in hex and decimal.
END
  This indicates to the assembler the end of the source (asm) file.
  The END directive is the last line of an 8051 program.
  the code anything after the END directive is ignored by the assembler.

## Slide 52: Assembler directive
EQU (equate)
  This is used to define a constant without occupying a memory location.
  When the label appears in the program, its constant value will be substituted for the label.
  COUNT EQU 32
  MOV R2, #COUNT

## Slide 53: Assembly language instruction
Data transfer instructions
Addressing modes
Data processing (arithmetic and logic)
Program flow instructions

## Slide 54: Data Transfer Instructions
MOV dest, source dest  source
Stack instructions
  PUSH byte ;increment stack pointer, ;move byte on stack
  POP byte ;move from stack to byte, ;decrement stack pointer
Exchange instructions
  XCH A, byte ;exchange accumulator and byte
  XCHD A, byte ;
  The XCHD instruction exchanges the low-order nibble of the accumulator with the low-order nibble of the specified internal RAM location. The internal RAM is accessed indirectly through R0 or R1.

## Slide 55: Addressing Modes
Addressing Modes: Immediate, Register, Direct, Register indirect.
Immediate Mode – The source operand is a constant
  mov A, #0 ;put 0 in the accumulator
  ;A = 00000000
  mov R4, #11h ;put 11hex in the R4 register
  ;R4 = 00010001
Register Addressing – either source or destination is one of CPU register.
MOV R0,A
  MOV A,R7

## Slide 56: Addressing Modes
Direct Mode – specify data in RAM by its 8-bit address.
  Mov A, 70h ; copy contents of RAM at 70h to A
  Mov R0,40h ; copy contents of RAM at 40h to R0
Register Indirect – the address of the source or destination is specified in registers. Only R0 and R1 used for this purpose.
  MOV A,@R0 ;move contents of RAM whose
;address is held by R0 into A

## Slide 57: Data Processing Instructions
Arithmetic Instructions
  Affect the flags, such as Carry Flag (CY), Overflow Flag (OV) etc, in the PSW register.

## Slide 58: Logic Instructions
Bitwise logic operations
  (AND, OR, XOR, NOT)
ANL  AND
ORL  OR
XRL  XOR
CPL  Complement

## Slide 59: Other Logic Instructions
CLR - clear
RL – rotate left
RLC – rotate left through Carry
RR – rotate right
RRC – rotate right through Carry
SWAP – swap accumulator nibbles
mov A, #72h ; A  72h
SWAP A ; A  27h

## Slide 60: Rotate
Rotate instructions operate only on A
RL A
Mov A,#0F0 ; A 11110000
RL A ; A 11100001
RR A
Mov A,#0F0 ; A 11110000
RR A ; A 01111000

## Slide 61: Rotate through Carry
RRC A
MOV A, #0A9H ; A  A9
ADD A, #14H ; A  BD (10111101), C0
RRC A ; A  01011110, C1
RLC A
MOV A, #3CH ; A  3CH(00111100)
SETB C ; C  1
RLC A ; A  01111001, C0
C
C

## Slide 62: Program flow instructions
Unconditional jumps (“go to”):
  The unconditional jump is a jump in which control is transferred unconditionally to the target location.
Conditional jumps:
  Jump only if a certain condition is met
Call and return

## Slide 63: Unconditional jump instructions
In the 8051 there are two unconditional jumps:
  LJMP (long jump) and SJMP (short jump)
LJMP (long jump)
  3-byte instruction
  First byte is the opcode
  Second and third bytes represent the 16-bit target address
    Any memory location from 0000 to FFFFH
SJMP (short jump)
  2-byte instruction
  First byte is the opcode
  Second byte is the relative target address
    The relative address 00 to FFH is divided into forward and backward jumps

## Slide 64: Unconditional jump instructions Application
Unconditional jump instructions Application
  Infinite Loop: Microcontroller application programs are almost always infinite loops.
START: MOV C, P3.7
MOV P1.6, C
SJMP START

## Slide 65: Conditional Jumps
These instructions cause a jump to occur only if a condition is true. Otherwise, program execution continues with the next instruction.
LOOP:MOV A, P1
JZ LOOP ;if A=0,goto LOOP, else goto next instruction
MOV B, A

## Slide 66: Conditional jumps

## Slide 67: More Conditional Jumps

## Slide 68: Iterative Loops
For A = 0 to 4 do
{…}
CLR A
LOOP: ...
INC A
CJNE A, #4, LOOP
For A = 4 to 1 do
{…}
MOV R0, #4
LOOP: ...
DJNZ R0, LOOP

## Slide 69: CALL INSTRUCTIONS
Call instruction is used to call subroutine
  Subroutines are often used to perform tasks that need to be performed frequently.
  This makes a program more structured in addition to saving memory space.
LCALL (long call)
  3-byte instruction
    First byte is the opcode
    Second and third bytes are used for address of target subroutine (Subroutine is located anywhere within 64K byte address space)

## Slide 70: Call and Return
Call is similar to a jump, but
  Call pushes PC on stack before branching
lcall <address > ; stack  PC
Return is also similar to a jump, but
  Return instruction pops PC from stack to get address to return to
    ret ; PC  stack

## Slide 71: Call and Return
Main: ...
lcall sublabel
...
...
sublabel: ...
...
ret
the subroutine
call to the subroutine